## Slide 1: “Applications of trajectory statistical methods (TSM)”
Dr PEDRO SALVADOR
Department of Environment - CIEMAT, Madrid, Spain
Regional Training Course on Source Identification and Apportionment of Air Particulate Matter (APM), Sacavem, Portugal, 2 – 6 June 2014

## Slide 2
Learning SURFER skills
Cluster Analysis: Cape Verde, a case study
RTA-CPF: Cape Verde, a case study
STRUCTURE OF THE PRESENTATION

## Slide 3
The algorithms of the TSM were programmed with FORTRAN77
The final data treatment was performed with EXCEL
The graphical representation of the products (trajectories, meteorological fields, RTA maps, RCF…) were performed with SURFER
MAIN COMPUTER TOOLS

## Slide 4
1- LEARNING SURFER SKILLS
SURFER is a comercial software for Windows
SURFER is a grid-based contouring and 3-D surface plotting images
LEARNING SURFER SKILLS
SURFER will help us to:
Plot back-trajectories over a regular geographic grid
Create and represent a regularly spaced grid of meteorological variables
Create and represent interpolated maps from a regularly spaced grid of variables
Represent CPF or Concentration Fields on a regularly spaced grid

## Slide 5
LOADING OUR BASE MAP
Open SURFER program
LEARNING SURFER SKILLS
Create a new Plot-Document: File-> New-> Plot -Document
Load a Base map: Map-> Base Map
Go to: C:\course\Practice1\World_BM.bln
Base maps are used to show geographic information
We will load the “World_BM.bln” base map which contains
all county boundaries on a Longitude-Latitude XY map

## Slide 6
REPRESENTING TRAJECTORIES ON THE BASE MAP
LEARNING SURFER SKILLS
Go to: C:\course\Practice1\PRACTICE 1.xls
Worksheet “3 TRAJECTORIES” contains the time steps coordinates of longitude
and latitude in columns for 3 trajectories
Represent a trajectory as a Post Map: Map-> Post Map-> New Post Map
Post maps show XY locations on a map with symbols and labels

## Slide 7
REPRESENTING TRAJECTORIES ON THE BASE MAP
LEARNING SURFER SKILLS
The properties of the trajectory can be changed here (symbol and size of the time steps,
coordinates of other trajectories…)
Select the Post Map in the left column, where all the objects of your map are displayed

## Slide 8
REPRESENTING TRAJECTORIES ON THE BASE MAP
LEARNING SURFER SKILLS
Let’s integrate the trajectory over the Base Map
Select al the objects to be integrated: Edit> Select All
Overlay the objects: Map-> Overlay Maps

## Slide 9
REPRESENTING TRAJECTORIES ON THE BASE MAP
LEARNING SURFER SKILLS
Select the Post Map in the left column and improve the trajectory (red points, 0.03 cm size)
Select the Limits option in the Post Map properties and make a zoom (Lon: 50ºW-0º, Lat: 0º-20ºN)

## Slide 10
REPRESENTING TRAJECTORIES ON THE BASE MAP
LEARNING SURFER SKILLS
EXERCISE: Represent the 3 trajectories of PRACTICE 1.xls
with different colours in an appropiated frame
Select the Limits option in the Base Map properties and make a zoom (Lon: 50ºW-0º, Lat: 10ºS-40ºN)
Overlay all the objects after representing the three trajectories
Select each Post Map (trajectories) and change its properties
Select the Axis properties and modify: Axis attributtes: 0.04 cm – Labels-> Font: 6 points – Ticks-> Major Ticks 0.10 cm - Scaling-> Major interval: 10 -> First major tick: 50…

## Slide 11
REPRESENTING METEOROLOGICAL FIELDS ON THE BASE MAP
LEARNING SURFER SKILLS
SURFER allows creating and representing a regularly spaced grid of variables
First of all it is necessary to create the grid file from an XYZ data file
We will use daily fields of meteorological variables (sea level pressure, 850 hPa geopotential height,…)
Go to: C:\course\Practice1\PRACTICE 1.xls
Worksheet “DAILY FIELDS” contains the dialy fields of geopotential height at the 850 hPa level for the 3 trajectories (13/Jul/2011, 24/Ene/2011 and 31/Jul/2011) at 12 UTC
Create the grid file: Grid-> Data
Select:
the columns of data XYZ
the name of the output grid file
the Kriging gridding method

## Slide 12
REPRESENTING METEOROLOGICAL FIELDS ON THE BASE MAP
LEARNING SURFER SKILLS
The grid file TRAJECTORY 1.grd has now been created
Create the contour map with this grid file: Map-> Contour Map-> New Contour Map
IMPORTANT: any map can be exported as an image file (*.wmf, *.emf,*.jpg,…):
File-> Export

## Slide 13
REPRESENTING METEOROLOGICAL FIELDS ON THE BASE MAP
LEARNING SURFER SKILLS
Select the Contours Map in the left column
Select the Level and Line options in the Contours Map -> Levels properties:
Reduce the interval between isolines to 10 hPa
Change the width of the isolines (0.01 cm)

## Slide 14
REPRESENTING METEOROLOGICAL FIELDS ON THE BASE MAP
LEARNING SURFER SKILLS
Select al the objects to be integrated: Edit-> Select All
Overlay the objects: Map-> Overlay Maps
Select the Limits option in the Base Map properties and make a zoom (Lon: 50ºW-20ºE, Lat: 10ºS-40ºN)

## Slide 15
REPRESENTING METEOROLOGICAL FIELDS ON THE BASE MAP
LEARNING SURFER SKILLS
EXERCISE: Represent the 3 geopotential height fields of PRACTICE 1.xls
together with their corresponding trajectories

## Slide 16
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
A k-means cluster analysis will be performed with the data base
of APM obtained at Cape Verde (CV)
138 data of PM10, Mineral dust and Marine aerosol contributions (PMF)
138 4-days (96 hourly time steps) back-trajectories with origin at 1500 m agl
A FORTRAN 77 program will be used to perform the cluster analysis
Results will be represented with SURFER
Each back-trajectory file can be found in: C:\course\Practice2\CA
with the format yyyyddmm.txt

## Slide 17
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
Open program: Compact Visual Fortran 6 -> Developer Studio
Open Workspace: File-> Open Workspace->
C:\course\Practice2\CA\CA.dsw
The “DATES.txt” file contains the
Dates of the trajectories with the format:
yyyymmdd
The “FIRST_CCENTERS.txt” file contains the
Time steps of the initial cluster centers

## Slide 18
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
Firstly, a 2-means CA will be performed for Cape Verde trajectories
2 trajectories with a different behaviour were selected by visual inspection
They are the 2 first trajectories of PRACTICE 1

## Slide 19
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
Go to: C:\course\Practice2\PRACTICE 2.xls
Worksheet “2 INITIAL CLUSTER CENTERS” contains the time steps coordinates (longitude and latitude) of the 2 trajectories in columns
Select and Copy the data
Open the “FIRST_CCENTERS.txt” file in the
left column of the Workspace
Copy the time steps data

## Slide 20
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
Execute the program:
Write the number of clusters: 2

## Slide 21
CLUSTER ANALYSIS
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY
The program generates a number of ASCII (text) files:
“CLUSTER CENTERS.txt” with the time steps of the final cluster centers
“RESULTS.txt” with the cluster assigned to each date/trajectory
“EXTRA INFORMATION.txt” with the number of trajectories assigned to each cluster and within, between and total variances
“Cluster X.txt” with the time steps of all the trajectories assigned to cluster X
Copy all these data files and paste in C:\course\Practice2\

## Slide 22
CLUSTER ANALYSIS
Open the SURFER program and load the Base map: Map-> Base Map
Go to: C:\course\Practice2\World_BM.bln
Represent the cluster centers as Post Maps: Map> Post Map-> New Post Map
Go to: C:\course\Practice2\CLUSTER CENTERS.txt
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 23
CLUSTER ANALYSIS
Represent the members of the cluster centers as Post Maps:
Map-> Post Map-> New Post Map
Go to: C:\course\Practice2\Cluster 1.txt and Cluster 2.txt
Cluster 1: Marines air flows
Cluster 2: Continental air flows
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 24
CLUSTER ANALYSIS
Analize the clustering process:
Go to: C:\course\Practice2\RESULTS.txt and open the file with Excel
The cluster assignment for each trajectory during the 4 iterations are showed
In most cases, the cluster assignment did not changed across the 4 iterations
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 25
CLUSTER ANALYSIS
Open the: C:\course\Practice2\PRACTICE 2.xls Excel file
Worksheet “PM10” contains the 138 concentration values of PM10, Mineral dust and Marine aerosol contributions (PMF)
Copy the ITER4 column from RESULTS.txt and paste in column F of
Worksheet “PM10” of PRACTICE 2.xls
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 26
CLUSTER ANALYSIS
Work with these data and analize the mean levels of PM10, Mineral dust and Marine aerosol attributed to each cluster
Preliminary results:
More frequent continental air flows (73%) than marine air flows (27%)
Higher contribution of Saharan dust (38.5 µg/m3) attributed to continental air flows
Higher contribution of Sea salt (19.8 µg/m3) attributed to marine air flows
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 27
CLUSTER ANALYSIS
EXERCISE: Perform a 3-means Cluster Analysis
Go to: C:\course\Practice2\PRACTICE 2.xls
Page “3 INITIAL CLUSTER CENTERS” contains the time steps coordinates (longitude and latitude) of the 3 trajectories in columns
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 28
CLUSTER ANALYSIS
EXERCISE: Perform a 3-means Cluster Analysis
Go to: C:\course\Practice2\PRACTICE 2.xls
Worksheet “3 INITIAL CLUSTER CENTERS” contains the time steps coordinates (longitude and latitude) of the 3 trajectories in columns
Cluster 1: Southern-Atlantic air flows
Cluster 2: Continental air flows
Cluster 3: Northern-Atlantic air flows
2- CLUSTER ANALYSIS: CAPE VERDE, A CASE STUDY

## Slide 29
3 – RESIDENCE TIME ANALYSIS: CAPE VERDE, A CASE STUDY
A Residence Time analysis will be performed with the data base
of APM obtained at Cape Verde (CV)
138 data of PM10, Mineral dust and Marine aerosol contributions (PMF)
138 4-days (96 hourly time steps) back-trajectories with origin at 1500 m agl
CPF will be computed for each cell of the grid
A 2º longitude x 2ºlatitude cell grid was superimposed over the region defined by
2ºN-60ºN and 49ºW-20ºE
RESIDENCE TIME ANALYSIS

## Slide 30
3 – RESIDENCE TIME ANALYSIS: CAPE VERDE, A CASE STUDY
A FORTRAN 77 program will be used to perform the RTA
RESIDENCE TIME ANALYSIS
Open program: Compact Visual Fortran 6 -> Developer Studio
Open Workspace: File-> Open Workspace->
C:\course\Practice3\RTA\RTA.dsw
The “INCIDENCE_DAYS.txt” file contains the
Dates of the “incidence days”
with the format: yyyymmdd
The “DATES.txt” file contains the
Dates of all the sampling days
with the format: yyyymmdd

## Slide 31
3 – RESIDENCE TIME ANALYSIS: CAPE VERDE, A CASE STUDY
RESIDENCE TIME ANALYSIS
Open the: C:\course\Practice3\PRACTICE 3.xls Excel file
Worksheet “PM10 data” contains the 138 concentration values of PM10, Mineral dust and Marine aerosol contributions (PMF)
Let us consider as “incidence days” for PM10,
days with concentrations higher than the 90th Percentile
Mean value of PM10 concentrations: 84.8 µg/m3
90th Percentile of PM10 concentrations: 195.0 µg/m3

## Slide 32
3 – RESIDENCE TIME ANALYSIS: CAPE VERDE, A CASE STUDY
RESIDENCE TIME ANALYSIS
Copy apart the DATE and PM10 columns
Re-order the data from the highest to the lowest value of PM10 concentrations
Select the dates of the incidence days:
PM10 concentrations > 195.0 µg/m3

## Slide 33
Copy the DATE column, open the DATES.TXT file in the left column of the Workspace, and paste the data
RESIDENCE TIME ANALYSIS
Copy the date values of the incidence days, open the INCIDENCE DATES.TXT file in the left column of the Workspace, and paste the data

## Slide 34
RESIDENCE TIME ANALYSIS
Execute the program:

## Slide 35
RESIDENCE TIME ANALYSIS
This program reads each back-trajectory file (in: C:\course\Practice3\RTA)
with the format yyyyddmm.txt, for all the sampling dates (DATES.txt) and
the Incidence days dates (INCIDENCE_DAYS.txt)
The number of time-steps residing on each grid cell is calculated for all the sampling dates (TS) and for the Incidence days dates (ID)
The number of trajectories contributing with time steps to each grid cell is calculated (Ntr)
For each grid cell with >1 time step-> CPF=(ID)/(TS)

## Slide 36
The program generates an ASCII (text) file:
“RTA_CV.txt” with the values of Ntr, TS, ID and CPF for each grid cell
RESIDENCE TIME ANALYSIS

## Slide 37
RESIDENCE TIME ANALYSIS
Go to: C:\course\Practice3\RTA\RTA_CV.txt and open the file with Excel
Copy the 5 columns and paste in the C:\course\Practice3\PRACTICE 3.xls Excel file in a new worksheet called “RTA”

## Slide 38
RESIDENCE TIME ANALYSIS
Copy the column B from worksheet “9 PF” of PRACTICE 3.xls and paste in column
G (next to the CPF values) of worksheet “RTA”
A 9 point filter is thus computed to smooth the CPF map
and preserve significant variations

## Slide 39
RESIDENCE TIME ANALYSIS
REPRESENTING THE CPF MAP
Open the SURFER program and load the Base map: Map-> Base Map
Go to: C:\course\Practice3\World_BM.bln
Represent the CPF as a Classed Post Map: Map> Post Map-> New Classed Post Map
Go to: C:\course\Practice3\PRACTICE 3.xls and pick: RTA worksheet
Select the 9 POINT FILTER
column as the Z variable
in the General options
Select the Classed Post in the left column where all the objects of your map are displayed
Select the Classes options :
5 classes
Binning Method: Equal intervals
Symbol: square
Syze: 0.08 cm

## Slide 40
RESIDENCE TIME ANALYSIS
REPRESENTING THE CPF MAP
Select al the objects to be integrated: Edit> Select All
Overlay the objects: Map-> Overlay Maps

## Slide 41
REPRESENTING THE CPF MAP
Select the Classed Post Map, click on the right mouse and Order Overlay-> Move to back
RESIDENCE TIME ANALYSIS
Select the Limits option in the Classed Post Map properties
and make a zoom (Lon: 50ºW-20ºE, Lat: 2ºS-60ºN)
Air masses passing over Mali, Mauritania and Senegal entail high concentration events of PM10 at Cape Verde

## Slide 42
REPRESENTING THE CPF MAP
RESIDENCE TIME ANALYSIS
Represent the composite 850 geopotential height field of the PM10 “high incidence days” as a Contour Map: Map> Contour Map-> New Contour Map
Create the Grid Data file: Grid-> Data
Go to: C:\course\Practice3\PRACTICE 3.xls and pick: SYNOP HI PM10 worksheet

## Slide 43
RESIDENCE TIME ANALYSIS
EXERCISE: Perform a RTA with “low incident days” for PM10
Go to: C:\course\Practice3\PRACTICE 3.xls
Worksheet “PM10 data” contains the 138 concentration values of PM10
Let us consider as “incidence days” for PM10,
days with concentrations lower than the 10th Percentile
Mean value of PM10 concentrations: 84.8 µg/m3
10th Percentile of PM10 concentrations: 23.6 µg/m3

## Slide 44
RESIDENCE TIME ANALYSIS
Air masses passing over south to southwestern atlantic areas entail low concentration events of PM10 at Cape Verde

## Slide 45
ACKNOWLEDGEMENTS
ACKNOWLEDGEMENTS
THANK YOU VERY MUCH FOR YOUR ATTENTION